## Slide 1: Adder design
going further . . .
exploring new design approaches

## Slide 2: Outline
Apply our CMOS circuit design skills for designing adders
A step-by-step process for improving performance wrt timing constraints
Interactive lecture where we play around designing adders in Microsoft Excel
Why Excel?
  Cell based like standard-cell design
  Excel logic functions can be used to validate adder functionality
  Unit delay model can be used to illustrate propagation delay
Types of adders
  Ripple-carry adder
  Carry generate and propagate prefix setup logic to improve speed
  Carry-skip adders
  Carry-lookahead adders
  Prefix tree adders, like Sklansky adders, Ladner-Fischer, Brent-Kung adders

## Slide 3: Datapath adder word slice
Bitslice 6
Bitslice 5
Bitslice 4
Bitslice 3
Bitslice 2
Bitslice 1
Adder word slice
Notes: This slide shows the datapath layout. We can see that the datapath is designed by 8 more or less identical bit slices, one for each bit. Each bit slice contains different functionalities, at the datapath level we can talk about functionality slices.
This is a design style that we are going to use in this course in some design examples concerning adder design. The use of bit slices to form functional arrays is sometimes referred to as iterative logic arrays, if all bit slices in the array are identical. This is a very efficient way of designing, since we only need to design one bit-slice cell to build a complete multi-bit array.
As I said, we shall apply this design style to the design of a full adder in a series of exercises later in the course.

## Slide 4: Iterative logic arrays: FULL ADDER
FA
a0
b0
cin
cout
Sum0
Design adder by using 8 instances of bit adder cell
CLK cycle time T
cout
a7
b7
a6
b6
a5
b5
a4
b4
a3
b3
a2
b2
a1
b1
a0
b0
Sum0
Sum1
Sum2
Sum3
FA
cin
FA
cout
FA
FA
Sum0
Sum1
Sum2
Sum3
Sum4
Sum5
Sum6
Sum7
FA
FA
FA
FA
Sum4
Sum5
Sum6
Sum7
Adder word slice
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
CLK
FF
FF
Notes: One of the main themes of this course is the design of n-bit adders. For starters, we will do that by designing the adder as an iterative logic array. For this, we need to design one Full Adder cell as the one shown here. We will use the methods discussed in this lecture to design the cell with MOSFETs from the Boolean truth table.
Then we will build an iterative logic array from many instances of this cell.
The two numbers to be added are enetered at the top. The carry-in is entered to the LSB (least significant bit) to the right. As the carry ripples from cell to cell, from right to left, the sums pop out at the bottom.

## Slide 5: Boolean truth table
You can check your Boolean expression by inserting it to the Boolean truth table first!
SUM expression already inserted as a hint on how to write logic in Excel!
SUM=OR(AND(A;B;CIN);AND(NOT(COUT);OR(A;B;CIN)))*1
(A, B, CIN, COUT to be replaced by work sheet cell coordinates)

## Slide 6
Text book full adder block solution
SUM LOGIC ”=OR(AND(A;B;C);AND(IN;OR(A;B;C)))*1”
carry cell
SUM cell
Ripple-carry adder design in Excel
This is a geometrical representation of a ripple-carry adder.
Each row in in Excel work sheet corresponds to 2.6 mm in ST 65 nm CMOS cell library.
Next task: implement your carry cell using the adder template where the SUM cell logic has already been implemented.
YOUR TASK IS
1) TO WRITE CARRY LOGIC EXPRESSION
INTO LSB CARRY CELL USING EXCEL AND/OR/NOT LOGIC FORMULA,
AND
2) CLICK-AND-DRAG TO GET 8 INSTANCES OF CARRY CELL
CARRY LOGIC ”=(LOGIC EXPRESSION)*1”

## Slide 7: Ripple-carry adder design in Excel
Next task: Validate your design by checking its functionality!
Does it work also for subtraction?

## Slide 8: Ripple-carry adder design in Excel
TIME AXIS
Teacher demo: illustrating the carry-ripple delay by introducing a timing axis, and by letting each cell row height represent a unit delay. CUT-AND-PASTE exercise.
Each row in Excel is a timing representation using unit-delay model.

## Slide 9: Ripple-carry adder design in Excel
Teacher demo: illustrating the carry-ripple delay by introducing a timing axis, and by letting each cell row height represent a unit delay. CUT-AND-PASTE exercise.
Each row in Excel is a timing representation using unit-delay model.
TIME AXIS

## Slide 10: Ripple-carry delay calculations
Full textbook solution as proposed in chapter 10 on adders
CIN
B
A
SUM
COUT
carry cell
SUM cell

## Slide 11: Ripple-carry delay calculations
Full textbook solution as proposed in chapter 10 on adders
SUM
SUM cell
CIN
B
A
carry cell
COUT

## Slide 12: Ripple-carry delay calculations
Redraw for identifying the critical timing path
SUM
SUM cell
CIN
B
A
carry cell
B
A
CIN
COUT

## Slide 13: Ripple-carry delay calculations
COUT
SUM
SUM cell
B
A
carry cell
B
A
CIN
CIN
COUT
Redraw for identifying the critical timing path
SUM
SUM cell
CIN
B
A
carry cell
B
A
CIN

## Slide 14: Ripple-carry delay calculations
Identifying the critical timing path
SUM
SUM cell
CIN
B
A
carry cell
B
A
CIN
COUT
SUM
SUM cell
B
A
carry cell
B
A
CIN
CIN
COUT
4
4
4
2
2
2
2
2
1
1
1
1
1
2
2
2
2
2
2
2
1
1
1
1
2
1
X
X1
X2
X2
X2

## Slide 15: Ripple-carry delay calculations
Critical timing path
SUM
SUM cell
CIN
B
A
carry cell
B
A
CIN
COUT
SUM
SUM cell
B
A
carry cell
B
A
CIN
CIN
COUT
X
X1
X2
X2
carry cell
gCIN=2, p=4
carry cell delay
d=4+2*(x+1)/2+1+4/x
X2

## Slide 16: Ripple-carry delay calculations
In the textbook there is a discussion on full adder cell MOSFET sizing!
Rather extreme sizing!

## Slide 17: Ripple-carry delay calculations
Critical timing path
SUM
SUM cell
CIN
B
A
carry cell
B
A
CIN
COUT
SUM
SUM cell
B
A
carry cell
B
A
CIN
CIN
COUT
8
8
8
4
4
4
2
2
1
1
X
X1
X2
X4
carry cell
gCIN=2, p=4
carry cell delay
d=4+2*(x+1)/2+1+4/x
X4

## Slide 18: Improving the design
Finding faster carry cells!
Less complicated cell with smaller number of MOSFETs!
We are going to accomplish this by preparing the carry cell input signals!
As an example: SUM=XOR(A;B;CIN),
here P=XOR(A;B) can be prefixed while we are waiting for the carry!

## Slide 19: Go back to Boolean truth table
NOTE: COUT=Generate+Propagate*CIN
FA
a0
b0
cin
cout
Sum0
Divide and conquer: Divide full adder cell into carry and SUM cells!
Design adder by using 8 instances of bit adder cell
G=AND(A;B)
P=XOR(A;B)
SUM=XOR(P;CIN)
cout
cin
AO21
G P
SUM XOR
SUM

## Slide 20: Using P and G half adder setup cells
cout
cin
Sum1
Sum2
Sum3
Sum4
Sum5
Sum6
Sum7
Sum8
HA
HA
HA
HA
HA
HA
HA
HA
g8
p8
g7
p7
g6
p6
g5
p5
g4
p4
g3
p3
g2
p2
g1
p1
a8
b8
a7
b7
a6
b6
a5
b5
a4
b4
a3
b3
a2
b2
a1
b1
Carry cell
Carry cell
Carry cell
Carry cell
Carry cell
Carry cell
Carry cell
Carry cell
SUM
XOR
SUM
XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR

## Slide 21: Using P and G half adder setup cells
cout
cin
Sum1
Sum2
Sum3
Sum4
Sum5
Sum6
Sum7
Sum8
HA
HA
HA
HA
HA
HA
HA
HA
g8
p8
g7
p7
g6
p6
g5
p5
g4
p4
g3
p3
g2
p2
g1
p1
a8
b8
a7
b7
a6
b6
a5
b5
a4
b4
a3
b3
a2
b2
a1
b1
AO21
AO21
AO21
AO21
AO21
AO21
AO21
AO21
SUM
XOR
SUM
XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR
SUM XOR

## Slide 22: Using P and G half adder setup cells
Empty row of cells, to be left blank until the next task
Fourth task: Enter G and P logic, enter carry AO21 logic and replace SUM cell logic with XOR logical function!
Note: P and G is never =1 at the same time! It is either propagate or generate, never both!
Therefore the AO logic expression in the C1:0 cells can be written very simple like =G1+P1*CIN!

## Slide 23: Using P and G half adder setup cells
Note: P and G is never =1 at the same time! It is either propagate or generate, never both!
Therefore the AO logic expression in the C1:0 cells can be written very simple like =G1+P1*CIN!
Next improvement is letting the combined propagate signal ripple along with the carry signal to the array output.
Why: The carry-skip adder!
Fifth task: Let the combined propagate signal ripple through the adder array along with the carry signal

## Slide 24: Carry-Skip Adder
Carry-ripple is slow through all N stages
Carry-skip allows carry to skip over groups of n bits
  Decision based on n-bit propagate signal
n-bit blocks
k=N/n number of n-bit blocks
N-bit adder
Verify the delay model given in eq. 10.13:

## Slide 25: Carry-Skip Adder
Carry-ripple is slow through all N stages
Carry-skip allows carry to skip over groups of n bits
  Decision based on n-bit propagate signal
n-bit blocks
k=N/n number of n-bit blocks
N-bit adder
For 32-bit adder we had 31*tAO; Now only tPG+14tAO + 3tMUX
Delay is cut in half!

## Slide 26: Analyzing the AOI21 cell
4
4
2
2
R
R
4
2
AOI21 cell
AOI21 cell
g=2, p=8/3
Let us make a non-inverting AO21 cell as a module and determine its g and p values
F
GENERATE
PROPAGATE
P
G
CIN=
6C
NORMALIZED DELAY CIN INPUT:
X
X2
R/x
3xC
CONCLUSION:
Non-inverting X4 AO21 cell has
internal parasitic delay p=7.7≈8
and logical effort g=0.5

## Slide 27: Using P and G half adder setup cells
Once we realize that the carry arriving at the adder block output is actually a block generate signal, we are ready for the next improvement step!
THE CARRY-LOOKAHEAD ADDER
Why is that so? Because if G8:1=1, a carry has been generated within the block!

## Slide 28: Carry-Lookahead Adder
Carry generate allows us to replace MUX with another AO21 gate.
”MUX”
k=N/n groups of n-bit blocks
n-bit blocks
N-bit adder
Verify the delay model given in eq. 10.14:
a7:0

## Slide 29: Propagate binary tree
&
&
&
&
&
&
&
P7
P5
P4
P3
P2
P1
P8
P6
P8:7
P6:5
P4:3
P2:1
P8:6
P4:1
P8:1
&
P2
&
&
P4
P3
&
&
P6
P5
&
&
P8
P7
P8:1
P2:1
P1
P4:1
P3:1
P6:1
P5:1
P7:1
Two ways of designing an 8-bit AND gate!
Which solution is the fastest?
In one solution the delay increases linearly with the number of inputs N,
in the other the delay increases as log2N,

## Slide 30: Carry-Lookahead Adder
So if we design the block-PROPAGATE AND-gate as a binary tree,
will the adder be any faster?
Yes or no?

## Slide 31: Propagate binary tree
No, it will not.
We still have to wait for BLOCK-GENERATE!
Unless it also can be designed as binary tree!

## Slide 32: G, P binary prefix-tree
G(7)
P(7)
G(5)
P(5)
G(4)
P(4)
G(3)
P(3)
G(2)
P(2)
G(1)
P(1)
G(8)
P(8)
G(6)
P(6)
G(2:1)
P(2:1)
G(6:5)
P(6:5)
G(2:1)
P(2:1)
G(6:5)
P(6:5)
G(4:1)
P(4:1)
G(8:5)
P(8:5)
G(8:1)
P(8:1)
G(i:k)=G(i:j)+P(i:j)G(j:k)
P(i:k)=P(i:j)P(j:k)
G(i:j)
P(i:j)
G(j:k)
P(j:k)
The “dot operator” logic
G(i:k)=G(i:j)+P(i:j)G(j:k)
P(i:k)=P(i:j)P(j:k)
The “dot operator”
Use the “dot operator” to show that the output carry from the binary prefix-tree tree is equal to the carry output from a ripple-carry array! Expression shown at top!

## Slide 33: Summary
We have
introduced Microsoft Excel as a tool for studying adder designs
introduced Excel timing graphs
identified the generate/propagate behaviour of the addition
built a new G and P based adder using AO21 cells for the carry
built a 32-bit carry-skip adder with reduced propagation delay compared with the ripple-carry solution
introduced the carry–lookahead concept using block G and P
used a binary tree design to form the block P and G outputs
Next week: a close look at our G/P cell design name it the ”dot operator” and, see how it can be used to build pre-fix tree adders

## Slide 34: To think about until next Tuesday
Task 1: Try to appreciate the Excel adder design approach 
Task 2: Verify the carry-skip propagation delay formula given in textbook equation 10.13.
Task 3: Verify the carry-lookahead propagation delay formula given in textbook equation 10.14.
Task 4: Use the “dot operator” to show that the binary prefix-tree carry output is equal to the carry output from a ripple-carry array!

## Slide 35: Example: synthesized 32-bit ALU/adder layout