## Slide 1: Sequential circuit design with metastability
Lecture 11
October 3, 2017
Preliminary version

## Slide 2: Sequential Logic
Combinational logic
  output depends on current inputs
Combinatorial logic
in
out
Sequential logic
  output depends on current and previous inputs
  Requires separating previous, current, future
  Called state or tokens
  Examples: Finite state machine (FSM), pipeline
Combinatorial logic
in
out
clk
clk
Figure 1.67 from W&H

## Slide 3: Sequencing
If tokens move through pipeline at constant speed, no sequencing elements are necessary
Ex: fiber-optic cable
  Light pulses (tokens) are sent down cable
  Next pulse sent before first reaches end of cable
  No need for hardware to separate pulses
  But dispersion sets min time between pulses
This is called wave pipelining in circuits
In most circuits, dispersion is high
  Solution: delay fast tokens so they don’t catch up on slow ones.

## Slide 4: Sequencing overhead
Solution: Use flip-flops to delay fast tokens so they move through exactly one stage each cycle.
Drawback: Adds some delay also to the slow tokens
Thus, circuit is slower than just logic propagation delay
  Added delay is called sequencing overhead
Some people call this clocking overhead
  But it applies to asynchronous circuits too
  Inevitable side effect of maintaining sequence

## Slide 5: This lecture
Compute sequencing overhead with flip-flops
  Compute maximum clock frequency
  Also with clock skew
Understand causes of delays in flip-flops and abit about their design tradeoffs
  But not design them
Synchronization of asynchronous signals
  Metastability

## Slide 6: Return to adder example
Figure 1.67 from W&H

## Slide 7: Ripple-carry adder (from postlab 2)
A way of drawing
the same thing with less detail for
the combinational logic (CL)

## Slide 8: Sequencing with flip-flops
Goals today:
Given a certain CL determine the minimum possible Tc with and without clock skew.
Given certain fc, clock skew and flip-flops determine timing requirements on CL.
Fllip-flop: Edge-triggered (positive edge) holds data until next edge
Part of Figure 10.2 from W&H
Notes: You can also sequence with latches but we leave that out.

## Slide 9: Characterizing combinational logic
Propagation delay, tpd:
  Maximum time until output finally reaches VDD/2.
  Output is guaranteed not to change after tpd.
Contamination delay, tcd:
  Minimum time until output initially reaches VDD/2.
  Output is guaranteed not to change before tcd.
Figure 10.4 (a) from W&H
Notes: Contamination delay is important because we do not wamt tokens to catch up with each other!

## Slide 10: Contamination delay When is delay shorter than tpd?
3-input NAND gate, Example 4.2 from W&H, Figure 4.7

## Slide 11: Flip-flop operation and delays
Edge-triggered (positive edge) holds data until next positive clock edge.
Input is called D output is called Q.
Input D has to be ready before clock edge happens, so that correct data is read.
Input D has to be stable long enough after clock edge happened to be correctly locked by flip-flop.
From clock edge happening it takes some time until output Q is available, there is a maximum and a minimum delay.
Figure 10.4 (b) from W&H

## Slide 12: Flip-flop operation and delays
Abbreviation | Flip-flop delay
tpcq | Clk-to-Q propagation delay
tccq | Clk-to-Q contamination delay
tsetup | Setup time
thold | Hold time
sampling window, aperture
Setup time is always
positive.
Hold time can be
positive, zero or
negative.
Figure 10.4 (b) from W&H

## Slide 13: What is minimum Tc?
Abbreviation | Flip-flop delay
tpcq | Clk-to-Q propagation delay
tccq | Clk-to-Q contamination delay
tsetup | Setup time
thold | Hold time
tpd, tcd
Notes: You can also sequence with latches but we leave that out.

## Slide 14: What is minimum Tc?
tpd, tcd
Make sure result from CL is always there when next clock edge happens:
Otherwise there is a setup violation.
Notes: You can also sequence with latches but we leave that out.

## Slide 15: Maximum propagation delay
Figure 10.5 from W&H

## Slide 16: What is minimum Tc with clock skew?
Clock skew = difference in delay (arrival time) for clock signals.
We do not know which way the difference will go.
Make sure result from CL is always there anyways when next clock
edge happens
tpd, tcd
Figure 10.15 (a) from W&H
Notes: You can also sequence with latches but we leave that out.

## Slide 17: Maximum propagation delay with clock skew
  Decreases maximum propagation delay

## Slide 18: Another potential problem
tpd, tcd
What if result from CL changes before the previous result has been read?
Then tokens are merged and data is lost.
Notes: You can also sequence with latches but we leave that out.

## Slide 19: Minimum contamination celay
Figure 10.9 from W&H

## Slide 20: Hold violation with clock skew?
tpd, tcd
What if result from CL changes before the previous result has been read
and we have clock skew?
Then tokens are merged and data is lost.
Notes: You can also sequence with latches but we leave that out.

## Slide 21: Minimum contamination delay with clock skew
  Increases minimum contamination delay
Figure 10.15 (b) from W&H

## Slide 22: Is setup or hold violations worse?

## Slide 23: System balancing
A well-designed system is balanced
No need to overdesign one part if another part limits system performance.
Tradeoff between:
  CL: delays, area, power
  Flip-flop design: delays, area, power, metastability
  Clock generation and distribution: delay clock skew, area, power

## Slide 24: How design a flip-flop?
Important requirements:
  Data is always maintained and restored
  Short delays
  Low capacitive load on clocks signals
  Small
  Enable
  Reset/set (synchronous or asynchronous)
  Scan chain

## Slide 25: D-Latch Example
A MUX on the input allows us to either load new data or keep old data
Two C-switches make a simple MUX

## Slide 26: Using tri-state inverters
_
f
f
f
f
However, an inverter and a C-switch can be replaced by tri-state inverter
_

## Slide 27: D-Latch Design
Tristate feedback
  + Static
  Backdriving risk
Static latches are essential so that data
does not disappear because of leakage
D
_
f
f
_
f
f
_ Q
X

## Slide 28: D-Latch Design
D
_
f
f
_
f
f
Q
Buffered input
  + Fixes diffusion input
  + Makes latch noninverting
X

## Slide 29: D-Latch Design
D
X
_
f
f
_
f
f
Buffered output
  + No backdriving
Widely used in standard cells
  + Very robust (most important)
  Rather large
  Rather slow (1.5 – 2 FO4 delays)
  High clock loading
Q
Q

## Slide 30: D-type Flip-Flop Design
Flip-flop is built as pair of back-to-back latches
D
_
f
f
f
X
X
_
f
f
_
f
f
_ Q
Q
_
f

## Slide 31: D-type Flip-Flop Design
Data is transferred from master to slave when CLK=1
Q´
f=0
data
Q
Q´
f=1
data
Q
New data is received by master when CLK=0, while slave stores previous data
_
f
f
f
_
f

## Slide 32: Enable
Enable: ignore clock when en = 0
  Mux: increase latch D-Q delay
  Clock Gating: increase en setup time, skew

## Slide 33: Enable circuit implementation
Q
ENABLE
DATA
0
1
C
C
C
C
Q’
CLK
CLK

## Slide 34: Reset
Force output low when reset asserted
Synchronous vs. asynchronous

## Slide 35: Set/Reset
Set forces output high when enabled
Flip-flop with asynchronous set and reset

## Slide 36: HS65_LS_DFPRQ

## Slide 37
Master latch
with NOR2
Slave latch
with tristate NAND
Clock generation

## Slide 39: Master latch 2.6 um × 2.8 um
DATA
CPI
CPN
CPI
CPN
TO SLAVE
CP
RN
Tristate
Tristate
INV
2NOR
CPI
RN

## Slide 40: Slave latch 2.6um × 3.2um
FROM MASTER
CPI
CPN
RN
Q
INV
INV+TG
INV
Tristate NAND
INV

## Slide 41: DFF layout in cell library
2.6 um
4.0 um

## Slide 42: Summary
We took a step from combinatorial logic to sequential logic:
  CL delays
  FF delays
Setup and hold violations:
  Constraints on CL delays from fc, flip-flop delays and clock skew
System tradeoffs – don’t overdesign any part!
Edge-triggered flip-flop from two back-to-back latches: one master, one slave
  Enable
  Set/Reset
  Scan chains
Had a look at a D-type FF in STMicroelectronics cell library
Compared to a master/slave design using our design template.
  Results: 6.0 μm wide compared with ST 4.0 μm
Next up: synchronization and metastability