## Slide 1: Lecture 16
Introduction to Integrated Circuit Design
Course summary
Notes: In this first lecture of the introductory course in integrated circuit design, we are going to learn how to design CMOS logical gates with a certain functionality.
But first, let me just say a few words on the context where we will meet combinational logic in a design.

## Slide 2: Designing gates with switches
N-switch
A
A
nMOSFET
OFF
P-switch
A
A
pMOSFET
ON
input A is LOW
Already the first lecture we learnt how to design gates with switches
and in CMOS there are two complementary switches
&
&
≥1
AB
CD
Y
Inputs:
A, B, C, D
pMOS
pull-up
network
nMOS
pull-down
network
VDD
VSS
Inputs:
A, B, C, D
Y
N-switch
A
A
nMOSFET
ON
P-switch
A
A
pMOSFET
OFF
input A is HIGH
Notes: When we are designing our gates, we will at this initial stage consider the MOSFETs as switches. In CMOS, we have complementary pairs of p-channel and n-channel MOSFETs. They are our building blocks. Initially, we will consider the MOSFETs as ideal switches. That is actually enough for designing functionality!
Since there are two types of MOSFETs, there are also two types of switches: n-switches and p-switches.
The n-switch is ON for HIGH inputs, i.e. for logic ones. Electrically, a logic one corresponds to a positiv supply voltage, VDD, while a logic zero corresponds to GND, or VSS.
The p-switch is ON for LOW inputs, i.e. for logic zeroes. This ´”inverted” function is indicated by the inverting bubble on the switch and pMOSFET symbols. The input to the p-switch is marked A, but due to the bubble it is when Abar is HIGH that the switch is turned ON.

## Slide 3: Designing gates with switches
B
A
D
C
VDD
VSS
Y
pMOS
pull-up
network
Inputs:
A, B, C, D
&
&
≥1
AB
CD
Y
Already the first lecture we learnt how to design gates with switches
and in CMOS there are two complementary switches
According to de Morgan´s theorem
N-switch
A
A
nMOSFET
P-switch
A
A
pMOSFET
N-switch
A
A
nMOSFET
Notes: Personally, I always start by designing the pull-down network. The output is supposed to go low when AB plus CD is HIGH. Products are realized as switches in series, since both switches need to be ON for the path to conduct. In this case, we have two parallel paths, each with two switches in series.

## Slide 4: Designing gates with switches
VDD
Y
&
&
≥1
AB
CD
Y
Already the first lecture we learnt how to design gates with switches
and in CMOS there are two complementary switches
According to de Morgan´s theorem
N-switch
A
A
nMOSFET
P-switch
A
A
pMOSFET
N-switch
A
A
nMOSFET
B
A
D
C
A
C
B
D
VDD
VSS
Y
Notes: Personally, I always start by designing the pull-down network. The output is supposed to go low when AB plus CD is HIGH. Products are realized as switches in series, since both switches need to be ON for the path to conduct. In this case, we have two parallel paths, each with two switches in series.

## Slide 5: Designing gates with switches
VDD
&
&
≥1
AB
CD
Y
Already the first lecture we learnt how to design gates with switches
and in CMOS there are two complementary switches
According to de Morgan´s theorem
N-switch
A
A
nMOSFET
P-switch
A
A
pMOSFET
N-switch
A
A
nMOSFET
B
A
D
C
A
C
B
D
VDD
VSS
Y
Notes: Personally, I always start by designing the pull-down network. The output is supposed to go low when AB plus CD is HIGH. Products are realized as switches in series, since both switches need to be ON for the path to conduct. In this case, we have two parallel paths, each with two switches in series.

## Slide 6: Layout and Euler paths

## Slide 7: Fabrication
Chips are built in huge factories called fabs
Contain clean rooms as large as football fields
Courtesy of IBM Corporation. Unauthorized use not permitted.

## Slide 8: Inverter mask set and fabrication
P-type silicon substrate
N-well
Active areas
P+ select
Poly gate
Contact cuts
Metal wires

## Slide 9: MOSFET – a square-law device
MOSFET transfer characteristic

## Slide 10: MOSFET models
VGS
Linear region
Saturation region
OFF region
VDS
IDS
Saturation region
Linear region
OFF region
OFF
ON
Models can predict IDS for any VGS/VDS
VDS
Max current
Output characteristic

## Slide 11: CMOS Inverter
VDD
VSW
VDD
VTN
VDD+VTP
0
0
VOUT
VIN
VSW
DV
Equal saturation currents
yields the switching voltage

## Slide 12: CMOS Inverter
1
1/2
VDD
1/4
3/4
0
0
VOUT
VIN
Simplify and assume VTN=-VTP=VDD/4
VSW
1/2

## Slide 13: NAND/NOR VTC
VOUT
Which VTC is NAND and which VTC is NOR?
VDD
0
VIN
NAND
NOR
NOR3
NAND3
1
3/8
1/4
3/4
5/8
0

## Slide 14: CMOS Inverter – Noise margins
1
1/2
VDD
1/4
3/4
0
0
VOUT
VIN
Simplify and assume VTN=-VTP=VDD/4
VSW
1/2
-1
-1
½-1/16
½-1/16
Non-valid
input region
1/16
1/16
Valid output
regions

## Slide 15: Switching the inverter
VDD
VSS
CL
VIN
VOUT
OFF
ON
VIN=HIGH
ON
OFF
VIN=LOW

## Slide 16: Defining the effective resistance . . .
Reff=VDD/IDSAT,max
IDSAT,max
VDD=1.2 V
N-channel device - IDSAT,max = 600 mA/mm
IDS
VDS
VDD
Slope Geff =1/Reff
Reff
VDD
CG
Defining the ideal, non-parasitic delay
tau = 0.7ReffCG= 5 ps in 65 nm CMOS
. . . and reference delay
tau
Notes: During the lecture, we will exercise with some more examples, like these suggested here: the 3+1 AND-OR-INVERT, and the 3+1 OR-AND-INVERT, as well as some more examples similar to those just shown.

## Slide 17: FO4 delay
The FO4 propagation delay becomes
X1
X1
Reff
CD
VDD
X1
X1
X1
CG
CG
CG
CG

## Slide 18: Defining logical effort
NAND3
NOR3
B
A
B
A
C
C
2
2
R
R
2
3
3
3
6
6
6
1
1
1
R
R

## Slide 19: Wire delay
R1
R2
Vin
C2
C1
Each resistance is multiplied by its downstream capacitance!
Or: Each capacitance is multiplied by its upstream capacitance!
V1
V2
R1
R2
Vin
C2
C1

## Slide 20: Sizing the driver
X
driver inverter
receiver inverter
CW/2
RW
CW/2
Wire p-model
C
pinvC
R
Start by defining wire effort

## Slide 21: Repeater insertion
X120
driver inverter
receiver inverter
X120
X120
R/m, C/m
R/m, C/m
Minimum for ∂d/ ∂m=0, i.e. for
Minimum normalized delay is d=4√WE.
driver model
receiver model
CW/2
RW
CW/2
Wire p-model
C
pinvC
R
C
driver model
receiver model
CW/2
RW
CW/2
Wire p-model
C
pinvC
R
C

## Slide 22: Divide and conquer
If they ask for the difference between x+a and x+b, i.e. a-b, we do not need to calculate x!
Branch contribution to delay is branch capacitance times upstream resistance
Total Elmore time constant is then 39RC/16≈2.5RC

## Slide 23: Divide and conquer
The wire to the other receiver is shorter, only ¾ of the other wire length
Hence, the main path to the other receiver has resistance 3R/4 and capacitance 3C/4
Main path delay contribution is found to be 22RC/16, and branch contribution is 15RC/16
Total Elmore time constant is then 37RC/16≈2.3RC

## Slide 24: The dot operator
G7
P7
G5
P5
G4
P4
G3
P3
G2
P2
G1
P1
G8
P8
G6
P6
G2:1
P2:1
G6:5
P6:5
G4:3
P4:3
G8:7
P8:7
G4:1
P4:1
G8:5
P8:5
G8:1
P8:1
&
&
&
P5
P6
&
P7
P8
P6:5
P8:7
&
&
&
P2
P4
P1
P3
P2:1
P4:3
P4:1
P8:5
P8:1
Show that
The “dot operator” is associative and idempotent
Show that

## Slide 25: The dot operator
Properties of the dot operator
  Associativity i.e. parallelization
  Easy to prove since logical OR and AND operations are associative
    With the definition Gi becomes the carry-out signal at stage i of an adder
  The operation is idempotent
  which implies
    where i≥j and m≥n

## Slide 26: 32-bit carry skip adder
Identify worst-case propagation delay for 32-bit adder!
For N-bit adder built with k n-bit blocks!
cout
+
ADD/SUB logic
Bit P, G
P8:1
cin
+
ADD/SUB logic
Bit P, G
P16:9
+
ADD/SUB logic
Bit P, G
P24:17
+
ADD/SUB logic
Bit P, G
P32:25
a8:1 b8:1
a16:9 b16:9
a24:17 b24:17
a32:25 b32:25
Sum8:1
Sum16:9
Sum24:17
Sum32:25
1
0
1
0
1
0
1
0
Determine the worst case delay!
tpg

## Slide 27: 32-bit carry-lookahead adder
&
≥1
&
≥1
&
≥1
cout
+
ADD/SUB logic
Bit P, G
G8:1
P8:1
cin
a8:1 b8:1
a16:9 b16:9
Sum8:1
+
ADD/SUB logic
Bit P, G
a24:17 b24:17
Sum24:17
+
ADD/SUB logic
Bit P, G
G32:25
P32:25
a32:25 b32:25
Sum32:25
+
ADD/SUB logic
Bit P, G
G16:9
P16:9
Sum16:9
&
≥1
G24:17
P24:17
tpg
tpg(n)
tpg(n)
tpg(n)

## Slide 28: Sklansky adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1←CIN
Determine the worst case delay!
Logic levels L=4
Extra levels l=0
Fanout 2f+1=9
f=3
Wire tracks 2t=1
t=0
l+f+t=L-1=3
(0, 3, 0)

## Slide 29: Example: synthesized 32-bit ALU layout

## Slide 30: Optimization – Questions and answers
Question: How should the p-channel width be chosen wrt the n-channel width in an inverter to minimize the average FO4 rise and fall delays if the hole mobility mh is only half the electron mobility me?
Answer. It should be 1.4 times wider, because

## Slide 31: Optimization – Questions and answers
Question: How should VDD be chosen wrt to VT to the minimize energy-delay product?
Answer: It should be three times larger, because the energy*delay product

## Slide 32: Optimization – Questions and answers
Question: What size (i.e. effective resistance) should we assign the inverter wrt the wire resistance to minimize the wire delay?
Answer: Using the Elmore delay model, the normalized wire delay

## Slide 33: Optimization – Questions and answers
Question: How many repeaters should we insert to minimize the delay caused by a long wire?
Answer: The part of the wire delay that depends on the number of repeaters, m,

## Slide 34: Optimization – Questions and answers
Question: What would be the most efficient block size for building a 32-bit carry-skip adder?
Answer: Assuming that the 32-bit adder is built by n-bit blocks using 32/n multiplexers, the worst case delay for calculating the most significant sum when a carry is generated in the least significant bit, is
If efficient muxes with tMUX=tAO could be used, 4-bit blocks would be most efficient. However, if muxes are slow due to their complexity, say tMUX=4tAO, then 8-bit blocks would be most efficient.

## Slide 35: Optimization – Questions and answers
Question: What if we were to build a 16-bit AND gate using n-input NAND/ NOR-gate combinations, what would be the most efficient number of gate inputs to minimize the delay? (Reminder: )
Answer: Since the normalized delay through n-bit NAND gates and NOR gates can be written
the NAND/NOR pair delay can be written dpair=3m+1. With a logical depth, N, given by nN=16, the total normalized delay can be written
However, the number of inputs must in this case be a multiple of 2, so our choice is to use 2- or 4-input gates; both resulting in about the same delay, with a minor advantage for the 4-input solution.

## Slide 36: Optimization – Questions and answers
Question: What if we were to build a 16-bit AND gate using n-input NAND/ NOR-gate combinations, what would be the most efficient number of gate inputs to minimize the delay? (Reminder: )
16-bit AND gate
16-bit AND gate
2-input NAND-NOR gates
4-input NAND-NOR gates

## Slide 37
Optimization – Summary
Function to
be optimized
p-MOSFET capacitance increases with p-channel width
Switching energy increases when VDD is increased
In wire delay, increasing source resistance means longer time to charge wire cap
Wire delay increases with number of repeaters
In carry-skip adders, block delay increases with increasing block size
In binary tree logic, stage delay increases with number of gate inputs
p-MOSFET resistance decreases with p-channel width
Switching delay decreases when VDD is increased
In wire delay, increasing source resistance means less gate cap
Wire delay decreases with length of wire segment
In carry-skip adders, multiplexer delay is reduced as their number decreases with increasing block size
In binary tree logic, logic depth, i.e. number of stages, is reduced with increasing number of gate inputs
x
Input variable
Arbitrary units
y
xopt

## Slide 38: End of course wrap-up lecture!
Q & A?
Notes: In this lecture, I have given you a little teaser of what this course is all about, on how to design CMOS logic gates, and how to put cells together to build multi-bit logic arrays. We will do a lot more of this during the course.
In this introduction, focus has been on functioanlity. Later, we will go into details about performance in terms of speed and power dissipation.
Questions you might have will answered, and problems you might have encountered will be discussed during the lecture.
Thank you very much for listening!