## Slide 1: Adder wrap-up
Lecture 14
2017

## Slide 2: Purpose of todays lecture
To learn how to design a 32-bit adder/subtractor where all sum cells have received their incoming carry signals after only 5 AND-OR delay units! Will be synthesized in Methods course.
The 5 units delay is to be compared to the delay of a ripple-carry adder: 31 AND-OR units delay, see figure below.
Or a ripple-carry lookahead adder with 17 AND-OR unit delays
+
+
+
+
a8:1 b8:1
a16:9 b16:9
a24:17 b24:17
a32:25 b32:25
Sum8:1
Sum16:9
Sum24:17
Sum32:25
cin
cout

## Slide 3: Ripple-carry timing
And that you have made yourself familiar with the timing of such a ripple-carry adder.

## Slide 4: 32-bit carry skip adder
cout
+
ADD/SUB logic
Bit P, G
P8:1
cin
+
ADD/SUB logic
Bit P, G
P16:9
+
ADD/SUB logic
Bit P, G
P24:17
+
ADD/SUB logic
Bit P, G
P32:25
a8:1 b8:1
a16:9 b16:9
a24:17 b24:17
a32:25 b32:25
Sum8:1
Sum16:9
Sum24:17
Sum32:25
1
0
1
0
1
0
1
0
Identify worst-case propagation delay for 32-bit adder!
For N-bit adder built with k n-bit blocks!
Determine the worst case delay!
tpg
The delay between the generation of a carry in the least significant bit (LSB)
until the most significant SUM is calculated!!

## Slide 5: 32-bit carry skip adder
cout
+
ADD/SUB logic
Bit P, G
P8:1
cin
+
ADD/SUB logic
Bit P, G
P16:9
+
ADD/SUB logic
Bit P, G
P24:17
+
ADD/SUB logic
Bit P, G
P32:25
a8:1 b8:1
a16:9 b16:9
a24:17 b24:17
a32:25 b32:25
Sum8:1
Sum16:9
Sum24:17
Sum32:25
1
0
1
0
1
0
1
0
Identify worst-case propagation delay for 32-bit adder!
For N-bit adder built with k n-bit blocks!
tpg
Determine the worst case delay!
The delay between the generation of a carry in the least significant bit (LSB)
until the most significant SUM is calculated!!

## Slide 6: Carry-lookahead adder
&
≥1
&
≥1
&
≥1
cout
+
ADD/SUB logic
Bit P, G
G8:1
P8:1
cin
a8:1 b8:1
a16:9 b16:9
Sum8:1
+
ADD/SUB logic
Bit P, G
a24:17 b24:17
Sum24:17
+
ADD/SUB logic
Bit P, G
G32:25
P32:25
a32:25 b32:25
Sum32:25
+
ADD/SUB logic
Bit P, G
G16:9
P16:9
Sum16:9
&
≥1
G24:17
P24:17
DELAY = tpg(n) = log2(n)*tAO= 3 tAO for n=8
tpg
tpg(n)
tpg(n)
tpg(n)
tpg(n)

## Slide 7: Carry-lookahead adder timing
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 8: Binary trees
G7
P7
G5
P5
G4
P4
G3
P3
G2
P2
G1
P1
G8
P8
G6
P6
G2:1
P2:1
G6:5
P6:5
G4:3
P4:3
G8:7
P8:7
G4:1
P4:1
G8:5
P8:5
G8:1
P8:1
&
&
&
P5
P6
&
P7
P8
P6:5
P8:7
&
&
&
P2
P4
P1
P3
P2:1
P4:3
P4:1
P8:5
P8:1
g(i:k)=g(i:j)+p(i:j)g(j:k)
p(i:k)=p(i:j)p(j:k)
g(i:j)
p(i:j)
g(j:k)
p(j:k)
The “dot operator”
Show that
&
P3
P2:1
&
P4
P4:1
P3:1
P2
P1
&
G7
P7
G5
P5
G4
P4
G3
P3
G2
P2
G1
P1
G8
P8
G6
P6
G2:1
P2:1
G6:1
P6:1
G4:1
P4:1
G8:1
P8:1
G3:1
P3:1
G7:1
P7:1
G5:1
P5:1

## Slide 9: Sklansky adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1←CIN
Determine the worst case delay!
Logic levels L=4
Extra levels l=0
Fanout 2f+1=9
f=3
Wire tracks 2t=1
t=0
l+f+t=L-1=3
(0, 3, 0)

## Slide 10: Ladner-Fischer adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1←CIN
Logic levels L=5
Extra levels l=1
Fanout 2f+1=5
f=2
Wire tracks 2t=1
t=0
l+f+t=L-1=3
(1, 2, 0)

## Slide 11: Kogge-Stone adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1←CIN
Logic levels L=4
Extra levels l=0
Fanout 2f+1=2
f=0
Wire tracks 2t=8
t=3
l+f+t=L-1=3
(0, 0, 3)

## Slide 12: Han-Carlson adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1←CIN
Logic levels L=5
Extra levels l=1
Fanout 2f+1=2
f=0
Wire tracks 2t=4
t=2
l+f+t=L-1=3
(1, 0, 2)

## Slide 13: Brent-Kung adder
16:0 15:0 14:0 13:0 12:0 11:0 10:0 9:0 8:0 7:0 6:0 5:0 4:0 3:0 2:0 1:0 0:0
16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 CIN
Logic levels L=6
Extra levels l=3
Fanout 2f+1=2
f=0
Wire tracks 2t=1
t=0
l+f+t=L-1=3
(3, 0, 0)

## Slide 14: Tree Adder Taxonomy
Extra logic levels
Extra fanout
Extra wire tracks

## Slide 15: Tree Adder Taxonomy
Extra logic levels
Extra wire tracks
Extra fanout

## Slide 16: Home ssignment 3 adder task

## Slide 17
64/32-bit Reconfigurable Intel adder ISSCC 2004 (paper 8.7)
A 4GHz 300mW 64b Integer Execution ALU with Dual Supply Voltages in 90 nm CMOS, Sanu Mathew, Mark Anders, Brad Bloechel, Trang Nguyen, Ram Krishnamurthy, Shekhar Borkar, Intel, Hillsboro, OR

## Slide 18: Summary
After this interactive lecture you will know about
Carry-skip adders, carry-lookahead adders and prefix-tree adders like Sklansky adders, etc.
You can identify the worst-case propagation delay for N-bit carry-skip and carry-lookahead adders built from k n-bit blocks
You can identify the worst-case delay for prefix-tree adders like Sklansky adders.
Using the same principles, you should also be able to do so for the unknown prefix-tree adder in home assignment 3.
Using the same principles, you should also be able to do so in the written exam for some of the other prefix-tree adders like Brent-Kung and Ladner-Fischer.

## Slide 19
Q & A