## Slide 1: Lecture 2
The MOSFET

## Slide 2: The MOSFET as a switch
In the digital world, the MOSFET is a switch that is either ON with conductance GON, or OFF with zero conductance, GOFF=0
source
drain
ON
S=1
GON
source
gate
source
gate
drain
drain
gate
source
gate
drain
source
drain
source
drain
OFF
S=0
GON
GOFF

## Slide 3: Lecture outline
In this lecture we are going to have a closer look at some basic properties of the MOSFET beyond the switch model
Why?
Because, even if the switch model is good enough for designing logic CMOS gates based on their functionality . . .
. . . it is not good enough for determining the performance in terms of switching speed and power dissipation

## Slide 4: Lecture outline
First we are going to learn how to calculate the voltage depen-dence of the ON resistance (or rather the ON conductance) of the MOSFET based on the principles of the field-effect.
Then we are going to learn why, for any gate voltage, there is a maximum current that a MOSFET switch can deliver or sink.

## Slide 5: MOSFET output and transfer characteristics
The MOSFET is basically a “square-law” device!
VDS
IDS
Output characteristics
OFF: IDS=0
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VGT2
gate voltage overdrive
Transfer characteristics
VGS
IDS
VT
VDD
The MOSFET is turned ON
but for each gate voltage there is a maximum current that the MOSFET can sink or deliver
VGT
gate voltage overdrive
VDSAT=
VGT

## Slide 6: The MOSFET structure
LD
LS
STI
drain
source
L is the channel length
L
The metal-oxide-semiconductor structure
Silicon substrate
oxide
Metal gate
STI
W, the channel width

## Slide 7: The MOSFET capacitances
The metal-oxide-semiconductor structure
that must be lumped to the available ckt nodes, i.e. to source and drain
STI
STI
L is the channel length
drain
source
LD
LS
W, the channel width
Cbottom
Csidewall
Cbottom
Csidewall
L
There is a distributed gate capacitance
And then we have the parasitic source and drain capacitances
Metal gate
Silicon substrate

## Slide 8
CGS
CGD
CD
CG
Equivalent electrical two-port circuit model
VGS
VDS
VSS
VSS
GON
Model for linear device
VGS
VDS
VSS
VSS
IDSAT
Model for saturated device
CG/2
CG/2
CGD=0
VGS
VDS
VSS
CG
VSS
Reff
“Average” model during switching of device output
CD
CD
where Cox is the gate insulator capacitance per unit area, typically 20 fF/mm2
where p is a certain fraction of the gate capacitance, typically p=1
The distributed gate to channel capacitance must be lumped to the available ckt nodes, i.e. to source and drain

## Slide 9: ON/OFF MOSFET operation
VDS
IDS
VDS=0
p-type substrate
source
drain
VGS=0
VS=0
drain
source
In this illustration of the MOSFET operation, the source and drain will be considered like two oceans of charge carriers isolated from each other through a potential barrier.

## Slide 10: ON/OFF MOSFET operation
drain
VDS
IDS
VDS=0
p-type substrate
source
drain
VGS=0
VS=0
source
OFF: IDS=0
In this illustration of the MOSFET operation, the source and drain will be considered like two oceans of charge carriers isolated from each other through a potential barrier.
What if we apply small drain voltage?
VGS=VT
However, applying a certain gate voltage called the threshold voltage VT will just about remove the barrier.
– The drain level is lowered, but the source is still isolated by the potential barrier!
drain
VDS>0
VDS>0
VGS>VT
Increasing the gate voltage beyond the threshold voltage will lower the potential barrier at the source even further and form a conducting channel between source and drain.
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow

## Slide 11: Calculating the ON conductance, GON
VDS
IDS
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS>0
VDS>0
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
For calculating the ON conductance GON, let´s have a look at the mobile charge in the channel!
QS
Mobile charge QS at source (per unit length):
Drain current: IDS=QS×vS
If we introduce the conductance parameter
The drain current can be written
Cox is the gate capacitance per unit area
W is the channel width
VGT =VGS-VT is the gate voltage overdrive
Cox is the gate capacitance per unit area
W is the channel width
VGT =VGS-VT is the gate voltage overdrive
m is the charge carrier mobility [cm2/Vs]
E=VDS/L is the electric field along the channel
In this illustration of the MOSFET operation, the source and drain will be considered like two oceans of charge carriers isolated from each other through a potential barrier.
, E=VDS/L
Charge carrier drift velocity at the source: vS=mE
vS
OFF: IDS=0

## Slide 12: Having a closer look along the channel
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VDS
IDS
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS>0
VDS>0
QS
Mobile charge QS at source (per unit length):
Cox is the gate capacitance per unit area
W is the channel width
VGT =VGS-VT is the gate voltage overdrive
m is the charge carrier mobility [cm2/Vs]
E=VDS/L is the electric field along the channel
vS
Mobile charge QD at drain (per unit length):
QD
Here, QD<QS because of the drain voltage.
Hence, drift velocity is higher at drain than at source, vD>vS,
This follows from the current being constant along the channel.
vD
(QS+QD)/2
v=mVDS/L
The result is a parabolic current model
w/ slope GON for small VDS
A thorough analysis based on the classical “gradual channel approximation” shows that the drain current is given by the average mobile charge density (QS+QD)/2 times the average drift velocity v=mVDS/L
OFF: IDS=0

## Slide 13: Understanding current saturation
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VDS
IDS
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS→VGT
VDS → VGT
QS
Mobile charge QS at source (per unit length):
Cox is the gate capacitance per unit area
W is the channel width
VGT =VGS-VT is the gate voltage overdrive
m is the charge carrier mobility [cm2/Vs]
E=VDS/L is the electric field along the channel
vS
Mobile charge QD at drain (per unit length):
QD≈0
Here, QD→0 when VDS→VGT Hence, drift velocity at drain approaches “infinity”, i.e. vD →∞.
This follows from the current being constant along the channel.
vD
≈QS/2
v=mVGT/L
The result is a parabolic current model
w/ slope GON for small VDS
Hence, the drain current IDS→ charge QS/2 × drift velocity mVGT/L as VDS→VGT.
The drain current seems to saturate as VDS→VGT
VGT
OFF: IDS=0

## Slide 14: Understanding current saturation
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VDS
IDS
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS>VGT
VDS > VGT
QS
vS
QD≈0
≈QS/2
v=mVGT/L
What if we increase the drain voltage beyond the gate voltage overdrive, i.e. VDS>VGT
Actually, the conditions within the channel does not change with the height of the “water fall” between the drain end of the channel and the drain!
The saturation voltage VDSAT is given by QD=0, → VDSAT=VGS-VT , i.e. the gate voltage overdrive VGT
Drain current stays constant!
The saturation current IDSAT is given by the gate voltage overdrive VGT squared!
The result is a parabolic current model
w/ slope GON for small VDS
VDSAT=
VGT
OFF: IDS=0
vD

## Slide 15: Piecewise linear MOSFET Model
What if we simplify the model, focusing on the two main behaviors of the MOSFET?
Linear behavior for small drain voltages - GON
Saturated behavior for large drain voltages - IDSAT
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VDS
IDS
VDSAT=
VGT
OFF: IDS=0
What if we decrease the gate voltage overdrive?
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS>VGT
VDS > VGT
QS
vS
QD≈0
≈QS/2
v=mVGT/L
vD
p-type substrate
source
drain
VGS>VT
VS=0
source
drain
VDS>VGT
VDS > VGT
QS
vS
QD≈0
≈QS/2
v=mVGT/L
vD

## Slide 16: MOSFET output and transfer characteristics
The MOSFET is basically a “square-law” device!
VDS
IDS
Output characteristics
OFF: IDS=0
The MOSFET is turned ON
and a current that appears
to be proportional to VDS
starts to flow
VGT2
gate voltage overdrive
Transfer characteristics
VGS
IDS
VT
VDD
The MOSFET is turned ON
but for each gate voltage there is a maximum current that the MOSFET can sink or deliver
VGT
gate voltage overdrive
VDSAT=
VGT

## Slide 17: Example
A fully turned on MOSFET has an on resistance of 1 kW. What is the maximum current that this device can deliver or sink? Assume VDD=1.2 V, and VT=0.3 V.
Maximum current that a
MOSFET can deliver or sink
VDS
IDS
VGT/2
Since the MOSFET is a square-law device (w/ parabolic I-V model) we know that the piecewise linear model breakpoint occurs at VGT/2.
Hence, maximum current is given by
Solution: We know that a long-channel MOSFET saturates for VDSAT=VGT=VGS-VT. Hence, in this case we have VDSAT=0.9 V.
VDSAT=
VGT

## Slide 18: Model can predict IDS for any VGS/VDS
VDS
VGS
VDD
VDD
VT
VDS=VDSAT=VGS-VT
Saturation region
Linear region
OFF
ON

## Slide 19: IDS can be plotted in 3D vs. VGS&VDS
VDS
VGS
IDS vs VDS: output characteristic
IDS vs VGS: transfer characteristic
VGS

## Slide 20: MOSFET regions of operation
Why are colored MOSFET regions of operation important?
Because they visualize the formula to use for estimating the drain durrent
SATURATION REGION
OFF REGION
CONTROL VOLTAGE VGS
OUTPUT VOLTAGE VDS
LINEAR REGION
ROFF=∞

## Slide 21
SATURATION REGION
OFF REGION
CONTROL VOLTAGE VGS
OUTPUT VOLTAGE VDS
LINEAR REGION
ROFF,N=∞
N-channel MOSFET
P-channel MOSFET
VGS
VDS
SATURATION REGION
OFF REGION
CONTROL VOLTAGE VGS
OUTPUT VOLTAGE VDS
LINEAR REGION
ROFF,P=∞

## Slide 22
N-channel MOSFET
P-channel MOSFET
VDS
IDS
IDSAT
saturation
IDSAT
saturation

## Slide 23: Summary
In this lecture, The MOSFET has been regarded as an electrically controlled ON/OFF switch.
Input and output voltages are referred to source
  Current controlling gate voltage VGS.
  The output drain voltage VDS.
The MOSFET current is a function of both voltages, VGS and VDS.
When ON, the MOSFET behaves
  like a resistor RON in its linear region,
  like a constant-current source IDSAT in its saturation region.
First-order approximation yields a square-law model for IDSAT=f(VGT2)
When OFF, there is a subthreshold leakage current, ISUB.
Very useful to color code the three regions of operation
  Red for OFF
  Green for ON and saturated (and blue for ON and linear operation)

## Slide 24
CGS
CGD
CGD
CGS
Equivalent electrical two-port circuit model
VGS
VDS
VSS
VSS
GON
Model for linear device
VGS
VDS
VSS
VSS
IDSAT
Model for saturated device
VGS
VDS
VSS
CG
VSS
Reff
“Average” model during switching of device output
The field-effect upon which the operation of a
MOSFET relies, gives the MOSFET a capacitive input!
In the linear region, the capacitance splits equally between source and drain
CG/2
CG/2
Q: Why use CGS=CG and not CGS=⅔CG?
A: Integers are easier to handle and there are parasitic overlap and fringing field caps there to motivate the approximation!
In the saturation region, the capacitance tilts towards the source!
⅔CG
CGD=0
The distributed gate to channel capacitance must be lumped to the available ckt nodes, i.e. to source and drain

## Slide 25
Effective resistances: 65 nm MOSFETs
Q: Why is there a difference between n- and p-channel effective resistances?
A: Hole mobility in p-channel device is only half of electron mobility in n-channel device!
IDS
N-channel device
VDS
VDSAT
VDD=1.2 V
IDS
P-channel device
VDS
VDSAT
VDD=1.2 V
RN,eff=2 kW.mm
RP,eff=4 kW.mm
IDSAT,max =
600 mA/mm
IDSAT,max =
300 mA/mm

## Slide 26: MOSFET gate capacitance
STI
STI
W, the channel width
L, the channel length
The capacitance between gate and channel, CG=WLCox, is intrinsic to the field effect!
In a 65 nm CMOS process, typically Cox=20 fF/mm2
When using fixed channel lengths, L=65 nm, as in digital designs, gate cap CG scales with channel width
Metal gate
drain
source
LD
LS
FYI, there are also parasitic overlap and fringing field capacitances between the gate and source/drain

## Slide 27: Source/drain parasitic capacitances
drain
LD
LS
STI
source
STI
Cbottom
Csidewall
Cbottom
Csidewall
The source and drain capacitances are extrinsic to the field effect!
Therefore regarded as parasitic capacitances, but are non-negligible, i.e. CD=pCG, where p≈1.
Sidewall caps due to source/drain lateral dimensions LS and LD, are usually small
Just as for the gate cap, we will consider source/drain caps scalable with channel width
Metal gate
W, the channel width

## Slide 28: 65 nm CMOS capacitances
Cox≈20 fF/um2
(corresponds to 1.2 nm effective oxide thickness)
60 nm effective channel length yields: CG=1.2 fF/um
Drain/source parasitic caps
The parasitic caps are of the same order of magnitude as the
gate capacitance, CS=CD=pCG
Generic approach is to use p=1 for simplicity
But sometimes p=0.5 or p=0.8!
channel
length, L
LS
LD
STI:
shallow trench isolation
W

## Slide 29
CGS
CGD
CD
CG
Equivalent electrical two-port circuit model
VGS
VDS
VSS
VSS
GON
Model for linear device
VGS
VDS
VSS
VSS
IDSAT
Model for saturated device
VGS
VDS
VSS
CG
VSS
Reff
“Average” model during switching of device output
CG/2
CG/2
The distributed gate to channel capacitance must be lumped to the available ckt nodes, i.e. source and drain
CGD=0
CD
CD
where Cox is the gate insulator capacitance per unit area, typically 20 fF/mm2
where p is a certain fraction of the gate capacitance, typically p=1

## Slide 30: The MOSFET in detail
A number of textbooks treat MOSFET models in great detail, including their physical background and short-comings due to short-channel effects in nanoscale devices

## Slide 31: How good is my model?
More parameters considering second-order effects must be included for fitting model to experimental data

## Slide 32: Determine k and VT @ VDS=100 mV
More parameters considering second-order effects must be included for fitting model to experimental data

## Slide 33: Determine k and VT @ VDS=100 mV
More parameters considering second-order effects must be included for fitting model to experimental data

## Slide 34: Include mobility roll-off

## Slide 35: Consider velocity saturation

## Slide 36: Consider drain-induced barrier-lowering (DIBL)

## Slide 37: Consider channel length modulation (CLM)

## Slide 38: Subthreshold leakage
Replot transfer characteristic on a semilogarithmic scale!

## Slide 39: Subthreshold leakage
Replot transfer characteristic on a semilogarithmic scale!
Subthreshold swing
S= 80 mV/decade
ION
IOFF

## Slide 40: Conclusion
In this lecture, we started considering MOSFET static properties
Three regions of operation
  Two ON regions: linear or saturated
  One OFF region: subthreshold
In second half of lecture we also considered dynamic properties
The intrinsic gate capacitance
The extrinsic, or parasitic drain capacitance
We came up with a two-port model including both static circuit elements (resistor or current-source), and dynamic elements, i.e. capacitances!