## Slide 1: CMOS Logic Gates a delay model
Introducing logical effort
Lecture 5

## Slide 2: Weekly schedule
Week 1
  Intro & the transistor
Week 2
  The CMOS inverter – one or more (tapered buffer)
Week 3
  Lab 1 Inverter schematic entry
  Delay model for CMOS gates – optimal path delay + ILAs
Week 4
  Lab 2 Carry circuit ILA schematic entry
  Physical design, layout, geometrical design rules
Week 5
  Lab 3 Carry circuit ILA layout and verification
  Wires, delay with wires & gates
Week 6
  Lab 4 Clock tree w. wires text entry & simulation
  Sequential & adders
Week 7
  Power & speeding up adders
Week 8
  Review

## Slide 3: Week 3
Monday lab1
  CMOS inverter static and dynamic
Tuesday
  Lecture Delay with gates, logical effort
  Postlab review lab 1
Thursday
  Prelab lab 2, Lecture on optimal path delay
  Tutorial POTW (Victor)
Friday Deadline prelab 2 –
  Schematic entry of carry ckt of full adder

## Slide 4: From MUD cards
Definitions
  Why is rise and fall time defined as 20 % to 80 %?
  Why is propagation delay defined from 50 % to 50 %?
Model of inverter
  Explanation of the step response model
  How to derive the equivalent model of one inverter
  Inverter output changes from input voltage confusing
One inverter driving on other inverter
  How resistance Reff and CG could give time constant?
  The relationship between CL and width.
Fanout-of-four (FO4) delay
  How to derive the delay
  How does scaling work with FO4
Tapered buffer (will review on Thursday)
  What is fanout (H) and the concept of optimum fanout.
  How calculate the number of inverters needed to minimize delay.

## Slide 5: Step-response model
VSS
VDD
VDD/2
IDS,P
VOUT
IDSAT,P
pMOS current flow in detail
VDD
VIN
ON
OFF
VIN=LOW
VOUT
CL
1. Charging the load capacitor through the p-channel MOSFET
Output rise delay
VIN goes LOW
VOUT goes HIGH
Notes: Note that the xcharging current is constant!

## Slide 6: Step-response model
VDD
VSS
CL
VIN
VOUT
2. Discharging the load capacitor through the n-channel MOSFET
OFF
ON
VIN=HIGH
Output fall delay
VDD
VDD/2
IDS,N
VOUT
nMOS current flow in detail
IDSAT,N
VIN goes HIGH
VOUT goes LOW
Notes: Note that the current is constant!

## Slide 7: Electrical model for saturated MOSFET (from lecture 2)
VG
VD
VS
VS
IDSAT
Model for saturated MOSFET
Valid for both nMOS and pMOS transistors
CD
CG
Notes: Model has been slightly updated so that it is correct also for pMOSFETs

## Slide 8: The inverter and its electrical model
Replace the MOSFETs with their equivalent electrical circuits!
VIN
VOUT
VSS
VDD
NMOS
VIN
VOUT
VSS
CGN
CDN
VSS
IDSN
IDSN
PMOS
VDD
CGP
CDP
VDD
IDSP

## Slide 9: The inverter and its electrical model
VIN
VOUT
VSS
VDD
NMOS
VIN
VOUT
VSS
CGN
CDN
VSS
IDSN
IDSN
PMOS
VDD
CGP
CDP
VDD
ISDP
Change the sign of the pMOS current so that all currents are positive
(We also made the pMOS voltages positive, although it is not necessary)

## Slide 10: The inverter and its electrical model
Place all capacitors to signal ground! Both rails are constant voltages, no dV/dt
VIN
VOUT
VSS
VDD
VIN
VOUT
VSS
VSS
IDSN
IDSN
VDD
VDD
ISDP
CG=CGN+CGP
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
CD=CDN+CDP

## Slide 11: The inverter and its electrical model
Eliminate VDD rail by inserting power supply to signal ground!
VIN
VOUT
VSS
VSS
IDSN
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
ISDP
VDD

## Slide 12: The inverter and its electrical model
Replace MOSFET constant-current sources with their effective resistances!
VIN
VOUT
VSS
VSS
RN,eff
Inverter input capacitance: CG=CGN+CGP; MOSFET gate capacitances add!
Inverter parasitic output capacitance: CD=CDN+CDP. Drain caps also add!
VIN
VOUT
VSS
VDD
CG=CGN+CGP
CD=CDN+CDP
RP,eff
VDD
RN,eff=2 kW.mm
RP,eff=4 kW.mm

## Slide 13: Inverter pair delay
Reff
VDD
Task: Calculate the inverter pair delay!
Note: identical inverters

## Slide 14: Inverter pair delay
Reff
VDD
Propagation delay:
All delay calculations are made wrt to this technology time constant tau (𝜏)
Equivalent electrical circuit for propagation delay calculations
CG
CD
VOUT
Reff and CG come from
different inverters to form
tau = 0.7 ReffCG
With fanout = 1, that is the
two inverters having the
same widths, tau is the
resulting time
constant.

## Slide 15: FO4 delay
Reff
VDD
Propagation delay:
Equivalent electrical circuit for propagation delay calculations
4CG
CD
VOUT
The load 4CG can be due to
four inverters with width = 1
or
one inverter with width = 4
or some other combination.
So CL is related to the
widths of the loading inverters.

## Slide 16: FO4 delay scaled
Reff /2
VDD
Propagation delay:
Make all the inverters twice as wide as before
also the loading ones
4 × 2CG = 8CG
2CD
VOUT

## Slide 17: FO4 delay scaled
2Reff
VDD
Propagation delay:
Make all the inverters half as wide as before – also the loading ones
4 × CG/2 =2CG
CD/2
VOUT

## Slide 18: Delay with any load
Reff
VDD
Propagation delay:
Equivalent electrical circuit for propagation delay calculations
CL
CD
VOUT
CL is the placeholder for the load capacitance.
CL can be due to anything capacitive connected to the driving inverter’s output.
If CL stems from inverters then CL is related to the
widths of the loading inverters.
h = electrical effort

## Slide 19: Background
In previous lecture, lecture 4, we have developed a propagation delay model for CMOS inverters.
For equal rise and fall delays, we have decided to use p-channel devices twice as wide as the n-channel device.
An n-channel MOSFET of unit width was assumed to have effective resistance R and gate capacitance C.
Hence, a p-channel device of two units width has the same effective resistance R, but gate capacitance 2C.
The inverter designed with such MOSFETs has input capacitance 3C, and equal pull-up and pull-down resistances.

## Slide 20: CMOS inverter –Transistor sizing
OUT
IN
3C
1 unit wide
2 units wide
3Cdrain
Note:
C is the gate capacitance of a MOSFET 1 unit wide
Cdrain is the drain capacitance of a MOSFET 1 unit wide

## Slide 21: CMOS inverter – cell sizing
OUT
IN
3C
1 unit wide
2 units wide
3Cdrain
VIN
VOUT
VIN
X2
X10

## Slide 22: CMOS inverter – cell sizing
VIN
N-well
VDD supply rail
VSS supply rail
VIN
VOUT
VIN
X2
X10
In ST cell library, size X refers to the input cap
(and for inverters also to the driving capability)!

## Slide 23: Inverter propagation delay model with load
Propagation delay definitions: rise and fall delays
tpdf
50%
We defined time constant tau equal to 5 ps in 65 nm CMOS technology. Furthermore, we introduced parasitic delay pinv=CD/CG, and electrical effort h=CL/CG.
VIN
VOUT
CL
tpdr
CG
CD

## Slide 24: Inverter propagation delay model
Two-port electrical representation of propagation delay model
VIN
VOUT
VSS
CG
VSS
CD
R
VDD

## Slide 25: Logic gate propagation delay model
Now we want to apply the same model to any CMOS logic gate
VIN
VOUT
VSS
CIN
VSS
Cpar
Reff
VDD
The pull-up and pull-down networks may have many different paths, but we want to design for equal effective resistance Reff in all paths!
But . . . what price do we have to pay for this in terms of input capacitance, CIN? And in parasitic capacitance, Cpar?
VDD
VSS
One input
OUT
CIN
pMOS
pull-up
network
nMOS
pull-down
network
Cpar
CL
CIN is the input capacitance for one of the inputs to the logic gate
Cpar is the total parasitic capacitance at the gate output

## Slide 26: Prerequisite: same worst-case resistance in all paths
Example: 2–input NAND gate
B
A
With 2/1 P vs N scaling
W
W
2W
2W
Worst case:
A=1 & B=1
=> Reff
Worst case:
A=0 & B=1
Or B=1 & A=1
=> Reff/2
Conclusion:
Need to change
widths in
p-net or n-net
(or both).
Many possible solutions with
same worst-case resistance
in n-net and p-net
W
W
W
W
2W
2W
2W
2W
If we don’t scale for same resistance we
cannot use equivalent gate model with Reff to the right of the switch.
Notes: If we do not perform this scaling we cannot move Reff to the right of the switch in the model!

## Slide 27: Logic gate propagation delay model
Now we want to apply the same model to any CMOS logic gate
VIN
VOUT
VSS
CIN
VSS
Cpar
Reff
VDD
VDD
VSS
Assume all pull-up/down paths have same resistance Reff. Obviously, the logic gate will have larger RC product than the inverter! What is the delay with load C L from one of the inputs to the logic gate?
As before, normalize to process time constant tau!
One Input
OUT
CIN
pMOS
pull-up
network
nMOS
pull-down
network
Cpar
CL
CL

## Slide 28: Logic gate propagation delay model
Now we want to apply the same model to any CMOS logic gate
Consider one delay term at a time!
One Input
VDD
VSS
OUT
nMOS
pull-down
network
Cpar
Here, we have defined the logical effort of a logic gate, g
The logical effort tells us how much larger the logic gate RC product is wrt inverter RC product!
pMOS
pull-up
network
CL
CIN

## Slide 29: Logic gate propagation delay model
To simplify, we suggest sizing MOSFETs for equal effective resistances, i.e. Reff=R
Consider one delay term at a time!
One Input
VDD
VSS
OUT
nMOS
pull-down
network
Cpar
This method conveniently separates the driving strength of a logic gate in terms of its logical effort, g, and its external load in terms of its electrical effort, h. And all with respect to the properties of the inverter.
pMOS
pull-up
network
CL
CIN

## Slide 30: Overview important concepts
d = f + p
f = gh
d: (normalized) stage delay
f: stage effort
g: logical effort
h: electrical effort
p: parasitic delay
All concepts related
to reference inverter
with (RCG)inv, pinv = CDinv/CGinv
The gate itself has parameters
CIN, Reff and Cpar
and is connected to load CL
If Reff ≠ Rinv
If Reff = Rinv
Note:
CIN can be different for different
gate inputs =>
Different g for different inputs!
Notes: Var tar 0.7:an vägen? Ah, men den är ju I tau som vi ska multiplicera med sen!

## Slide 31: Who invented logical effort?
Ivan Sutherland
Bob Sproull
“The father of computer graphics”
Together they worked on head-mounted displays.
Work on graphics hardware spurred the invention of logical effort

## Slide 32: Quiz time!
  Go to socrative.com
  Select Student login
  Go to room: “MCC0922018”

## Slide 33: Delay estimations using logical effort
Once the logical effort of a logic gate is known we can easily calculate the propagation delay of any critical timing path
Calculate delay
to here!
CMOS logic
X2
X4
X2 logic
g3, p3
X2 logic
g5, p5
X9 logic
g6, p6
X6 logic
g4, p4
Calculate delay!
p1, g1
p2=1, g2=1
Notes: NAND 3: g = 5/3 p = 3
Normalized delay d = 5/3x 2 + 3 + 1 + 1 +5/3x3 + 3 = 13 + 10/3 = 16 1/3

## Slide 34: Inverter propagation delay model
Two-port electrical representation of propagation delay model
Consider a unit size inverter with a unit size n-channel device and
a p-channel device of twice that width
VIN
VOUT
VSS
CG=3C
VSS
CD =pinvCG
R
VDD
OUT
IN
C
1
2
Cdrain
2C
2Cdrain
VIN
VOUT
1
R
3C
3Cdrain

## Slide 35: Effective resistance
Pull-up/down paths may have MOSFETs in series! Effective resistances add up!
VDD
1
1
1
IDS
R
R
R
Vout
Vout
Pull-down
network
Reff=3R
Solution: widen the MOSFETs to obtain effective resistance R!
N MOSFETs in series – make them 3 units wide!
VDD
3
3
3
IDS
R/3
R/3
R/3
Vout
Vout
Pull-down
network
Reff=R
Notes: This means that there are less current when transistors are in series! How can we understand that?

## Slide 36: Effective resistance
Pull-up/down paths may have MOSFETs in series! Effective resistances add up!
VDD
1
1
1
IDS
R
R
R
Vout
Vout
Pull-down
network
Cost:
Increased input capacitance!
3
3
3
IDS
R/3
R/3
R/3
Vout
Vout
Pull-down
network
Reff=3R
Reff=R
3C
3C
3C

## Slide 37: Effective resistance
Pull-up/down paths may have MOSFETs in series! Effective resistances add up! This is for p-channel devices!
VDD
2
2
2
IDS
R
R
R
Vout
VDD
Pull-up
network
Reff=3R
Vout
6
6
6
IDS
R/3
R/3
R/3
VDD
Again, widen MOSFET a factor 3 since they are 3 in series.
Cost:
Increased input capacitance!
Pull-up
network
Reff=R
6C
6C
6C
Vout
Vout

## Slide 38: Effective resistance
The propagation delay, tpd is defined as the worst-case delay, that is the longest delay.
(We did not mention that in lecture 4 because an inverter only has one input.)
Pull-up/down paths may have MOSFETs parallel! Effective resistances can be combined as resistors in parallel. But what is the worst-case resistance?
If A=0 & B=1
or A=1 & B=0
A
B
1
1
Vout
If A=1 & B=1
R/2
R
Vout
Vout
Worst case
because highest R

## Slide 39: Effective resistance
The same but for pMOS FETs in parallel.
If A=0 & B=1
or A=1 & B=0
A
B
2
2
Vout
R
Vout
If A=0 & B=0
R/2
Vout
Worst case

## Slide 40: The NAND/NOR VTC revisited
Which VTC is NAND and which VTC is NOR?
Assume all transistors have the same k and all three inputs switch together.
Now we can use our knowledge about Reff to find the effective kn and kp. Reff is inversely related to the maximum saturation current. So for entire path combined R gives us the inverse of the k factors.
0
VDD
VOUT
VSW
VDD
VTN
VDD+VTP
0
VIN
NAND
NOR
R/3 => kp = 3
R/3 => kn = 3
3R => kp = 1/3
3R => kn = 1/3
where x = kn/kp

## Slide 41
Example 1: The tri-state inverter
Vin
Vout
f
Vin
_
f
f
Tristate inverter symbol
4C
2C
Input cap = twice that of reference inverter: CG=6C
where C is gate capacitance of a unit width MOSFET
4
4
2
2
R
R
VIN
VOUT
VSS
6C
VSS
6Cdrain
R
VDD
While inverter RC-product is 3RC, tristate inverter
RC-product is 6RC, i.e. twice that of the inverter!
This ratio is defined as the “logical effort”, g, and g=6C/3C=2! Parasitic delay =6Cdrain/3C=2pinv
Make all MOSFETs twice as wide to cut effective resistance in half!
2Cdrain
4Cdrain
Parasitic output cap = 6Cdrain which is twice that of the unit inverter
Vout

## Slide 42
Example 1: The tri-state inverter
Vin
Vout
f
Vin
f
Tristate inverter symbol
Cdrain
2Cdrain
Say that we want input capacitance to be same as for the inverter! Then path resistances become 2R!
But parasitic delay and logical effort are the same!
Independent of gate sizing!
2R
2R
VIN
VOUT
VSS
3C
VSS
3Cdrain
2R
VDD
While inverter RC-product is 3RC, tristate inverter
RC-product is 6RC, i.e. twice that of the inverter!
Because
2
2
1
1
2C
C
Vout
Make all MOSFETs at original widths to keep input capacitances @ 3C.
_
f

## Slide 43: Example 2: 2+2 AND-OR-invert (AOI22)
F
B
C
D
D
VIN
VOUT
VSS
6C
VSS
12Cdrain
R
VDD
4
4
2
2
R
R
4
4
2
2
Make all MOSFETs twice as wide to cut effective resistance in half!
This gate also has logical effort, g=2 for all inputs A-D
Its parasitic RC-product p, the parasitic delay, is defined as
B
C
A
A
A
2C
4C
VIN
VOUT
1
R
3C
3Cdrain
Unit inverter

## Slide 44: Exercise: Calculate NAND2, NOR2 logical efforts
NAND2
NOR2
B
A
B
A

## Slide 45: Exercise: Calculate NAND3 & NOR3 logical efforts
NAND3
NOR2
B
A
B
A
C
C

## Slide 46: Exercise: compound gate OR-AND-INVERT 3+1
Note: Different inputs
to a gate can have different
logical efforts!

## Slide 47: OAI invert 3+1 gate done as quiz
Question 1: What is the logical effort of ABC inputs?
Question 2: What is the logical effort of D input?
Question 3: What is the parasitic delay expressed as p x pinv?
Work in small groups

## Slide 48: Exercise: compound gate OR-AND-INVERT 3+1 (solution)
6C R/3
6C R/3
6C R/3
2C R
2C R/2
2C R/2
2C R/2
2C R/2
Gate capacitance is proportional to
transistor width. Here we write out
capacitance for the scaling rather than width.
Drain capacitance is also proportional to width.

## Slide 49: Why all this?
Simplify delay calculations and making them technology independent!
CMOS logic
X2
X4
X2 logic
g=5/3, p=3
X2 logic
g=7/3, p=3
X9 logic
g=7/3, p=3
X6 logic
g=7/3, p=3
Calculate delay!
p1=4, g1=2
p2=1, g2=1
Propagation delay=18*tao=90 ps
In ST cell library, size X refers to the input cap!
Calculate delay
to here!

## Slide 50: Why all this?
Minimize path delays with gates other than inverters.
We will do that in lecture 6.

## Slide 51: Model for a non-inverting gate
The parasitic delay p=9
Logical effort g=0.5
CMOS logic
X2
X4
p1=4, g1=2
p2=1, g2=1
CL
CIN
2CIN
d = f + p should hold also for non-inverting gate
f is the part that depends on CL, f = gh where h is defined as CL/CIN
Thus fgate = CIN/CINinv× CL/CIN = ggate × hgate
p is static part of the delay: the part that does not depend on CL
We will do this on
Thursday!

## Slide 52: Overview important concepts
d = f + p
f = gh
d: (normalized) stage delay
f: stage effort
g: logical effort
h: electrical effort
p: parasitic delay
All concepts related
to reference inverter
with (RCG)inv, pinv = CDinv/CGinv
The gate itself has parameters
CIN, Reff and Cpar
and is connected to load CL
If Reff ≠ Rinv
If Reff = Rinv
Note:
CIN can be different for different
gate inputs =>
Different g for different inputs!

## Slide 53: Conclusion
In this lecture we have
Adapted the two-port delay model previously developed for inverters to any CMOS logic gate
Learnt how to size MOSFETs for equal worst case rise and fall delay
Noticed that logic gates have larger ReffCG products than inverters
Introduced two new concepts: logical effort and parasitic delay
Logical effort and parasitic delay quantifies
  Logical effort: (ReffCG)gate relative to (3RC)inv
  Parasitic delay: (ReffCpar)gate relative to (3RC)inv
Learnt how to calculate these parameters for any logic gate
Learnt how to calculate the electrical effort h= CLOAD/CIN
Learnt to calculate all propagation delays as a multiple of tau, where tau=5 ps in STMicroelectronics 65 nm CMOS process