## Slide 1: Path delay optizimization Review logical effort Prelab 2
Extending inverter delay optimization to other types of gates

## Slide 2: Week 3
Monday lab1
  CMOS inverter static and dynamic
Tuesday
  Lecture Delay with gates, logical effort
  Postlab review lab 1
Thursday
  Prelab lab 2, Lecture on optimal path delay
  Tutorial POTW (Victor)
Friday Deadline prelab 2
  Schematic entry of carry ckt of full adder

## Slide 3: From MUD cards
Too many efforts!
Inputs to the gate & logical effort
  How to calculate g, and, p, for different inputs.
  Not very clear on the input capacitance CIN. What if we have more than one input, which one should we choose?
Resistance and scaling
  Worst-case R for parallel and series connection.
  How to decide nMOS and pMOS widths during calculation of logical effort.
  For bigger schematics how to find worst-case scenario.
The constant part
  How to calculate Cpar for compound network..

## Slide 4: Too many efforts
f = g × h
Stage effort
or
Effort delay
Logical effort
Electrical effort
Only three efforts - all in the delay that depends on the external load CL!
Two of them combined make up the third one.
“h” is our variable, our “x”, as we will see later in this lecture.
And then there is a constant part, p, the parasitic delay
d = g × h + p
Compare to standard linear equation: y = k × x + m

## Slide 5: Graph of normalized inverter delay as a function of CL
CL
d
pinv
CIN = CL
Slope 1
CIN = ½ CL
Slope 2
CIN = 2CL
Slope ½
CIN = 4CL
Slope 1/4
Different slope for each
value of CIN, that is
each inverter size
d = pinv + (1/CIN) × CL

## Slide 6: Graph of normalized delay for inverter as a function of h
d
pinv
slope = 1
h = CL/CIN
h1
d = pinv + h

## Slide 7: Graph of normalized delay other gates
h = CL/CIN
d
pinv
p
Inverter:
slope = 1
g = 1
Other gate:
slope > 1
g > 1

## Slide 8: Example: NAND3

## Slide 9: Unclear things
Propagation delay, tpd, from one input signal to the output
is modeled with the normalized delay, d,
so CIN is the input capacitance for ONE of the gate inputs
(the one where we assume our input signal is entering).
Often all gate inputs have same CIN, but not always.

## Slide 10: Logic gate propagation delay model
Now we want to apply the same model to any CMOS logic gate
VIN
VOUT
VSS
CIN
VSS
Cpar
Reff
VDD
Note that already here Reff is placed to the right of the switch, which means we assume the the n-net path and p-net path worst-case resistances are the same.
VDD
VSS
One input
OUT
CIN
pMOS
pull-up
network
nMOS
pull-down
network
Cpar
CL
CIN is the input capacitance for one of the inputs to the logic gate
Cpar is the total parasitic capacitance at the gate output

## Slide 11: Logic gate propagation delay model
Now we want to apply the same model to any CMOS logic gate
VIN
VOUT
VSS
CIN
VSS
Cpar
Reff
VDD
VDD
VSS
Assume all pull-up/down paths have same resistance Reff. Obviously, the logic gate will have larger RC product than the inverter! What is the delay with load C L from one of the inputs to the logic gate?
As before, normalize to process time constant tau!
One Input
OUT
CIN
pMOS
pull-up
network
nMOS
pull-down
network
Cpar
CL
CL

## Slide 12: Logic gate propagation delay model
To simplify, we suggest sizing MOSFETs for equal effective resistances, i.e. Reff=R
Consider one delay term at a time!
One Input
VDD
VSS
OUT
nMOS
pull-down
network
Cpar
This method conveniently separates the driving strength of a logic gate in terms of its logical effort, g, and its external load in terms of its electrical effort, h. And all with respect to the properties of the inverter.
pMOS
pull-up
network
CL
CIN
One input
Same for
all inputs

## Slide 13: Deciding on resistances/scaling
Make all paths have the same resistance:
  Parallel paths:
    Assume that only one of any parallel path is conducting at a time
  Serial paths
    All transistors groups in series have to conduct for a path to be formed, but only one of any transistors in parallel within groups.
    As long as possible assign all transistors in series the same resistance (if there is no particular reason to do otherwise).

## Slide 14: Parasitic capacitances
All FETs have parasitic capacitances at drain and source
Our simplified model is that only parasitic capacitances at the output node contribute to parasitic delay – not entirely true.
Drain capacitances are proportional to transistor width & proportional to gate capacitance.
Approach to find parasitic delay p:
  Sum widths of all FETs connected to output node of gate.
  Divide by width of FETS connected to output node in inverter with same R.
  Multiply by pinv factor (CD/CG)

## Slide 15: Two complex gates for you to practice on (but not right now)
I will post the solution(s).

## Slide 16: Solution 1 complex gate 1
R/3
R/3
R/3
2R/3
R
R/2
R/2
R/2
Resistances for equal worst-case
path resistance R
6W
6W
6W
3W
W
2W
2W
2W
Corresponding widths
gc1 = (6+2)/3 =8/3
gc2 = (3+2)/3 =5/3
gp1 = (6+2)/3= 8/3
gp2 = (6+1)/3 = 7/3
p =(1+2+3+6)/3 pinv=
12/3 pinv = 4 pinv

## Slide 17: Solution 2 complex gate 1
R/4
R/2
R/4
R/2
R
R/2
R/2
R/2
Resistances for equal worst-case
path resistance R, p-net changed
8W
4W
8W
4W
W
2W
2W
2W
Corresponding widths
gc1 = (8+2)/3 =10/3
gc2 = (4+2)/3 =6/3
gp1 = (8+2)/3= 10/3
gp2 = (4+1)/3 = 5/3
p =(1+2+4+8)/3 pinv=
15/3 pinv = 5 pinv

## Slide 18: Complex gate 1 which solution is better?
It depends on which one is the critical input, the one on the critical path, that limits the speed, but unless it is p2, solution 1 is better. The resistances are more similar and also the parasitic delay is smaller.
Note: There was a constraint due to the physical layout that made us not put the p-net upside down (more about layout next week!).

## Slide 19: Solution 1 complex gate 2
6W
3W
6W
6W
W
3W
3W
3W
R/3
R/3
2R/3
R/3
R
R/3
R/3
R/3
Resistances for equal worst-case
path resistance R
Corresponding widths
gc1 = (3+3)/3 =2
gc2 = (6+3)/3 =3
gp1 = (3+3)/3= 2
gp2 = (6+3)/3 =3
gCoutin = 7/3
p =(1+3+6)/3 pinv=
10/3 pinv
R/3
2R/3
3W
3W

## Slide 20: Solution 2 complex gate 2
8W
4W
8W
4W
W
3W
3W
3W
R/4
R/4
R/2
R/2
R
R/3
R/3
R/3
Resistances for equal worst-case
path resistance R, p-net changed
Corresponding widths
gc1 = (3+4)/3 =7/3
gc2 = (8+3)/3 =11/3
gp1 = (3+4)/3= 7/3
gp2 = (8+3)/3 =11/3
gCoutin = 5/3
p =(1+3+4)/3 pinv=
8/3 pinv
R/3
R/2
3W
4W

## Slide 21: Complex gate 2 which solution is better?
Also here it depends on which one is the critical input (the one that is on the critical path and thus limits the speed), but from the schematic it looked like it would be coutin. In that case solution 2 is better. It also has a lower parasitic delay.

## Slide 22: Outline
A linear model for non-inverting gates
  Still d = gh + p, find p and g
  An example
Prelab 2 task
  ILAs
  The carry circuit
Review tapered buffer – only inverters
  Optimal h,optimal N
  Review the example
Path delay with other gates
  Optimal f
  An example

## Slide 23: Model for a non-inverting gate
The parasitic delay p=9
Logical effort g=0.5
CMOS logic
X2
X4
p1=4, g1=2
p2=1, g2=1
CL
CIN
2CIN
Linear model d = f + p = gh + p should hold also for non-inverting gate
f is the part that depends on CL, f = gh where h is defined as CL/CIN
Thus fgate = CIN/CINinv× CL/CIN = ggate × hgate
p is the static part of the delay: the part that does not depend on CL
Note that g < 1 is possible because here it depends on scaling between gates!

## Slide 24: Quiz about 3-input AND gate = 3-input NAND + inverter
&
X2
X6
g1=5/3, p1=3
g2=1, p2=1
CL
CIN
3CIN
What is pAND and gAND (the same for all three inputs)?
Work in small groups.
Enter your answers in Socrative: Room: MCC0922018.

## Slide 25: Prelab 2
Iterative Logic

## Slide 26: Prelab 2
MCC092 Integrated Circuit Design
Design task: design with MOSFETs the carry bit-cell for an 8-bit ripple-carry adder!
The 8-bit carry logic is to be implemented by an iterative logic array consisting of eight instances of the bit-cell that you have designed.
The carry bit-cell has three inputs (two bits a, b and a carry-in memory bit), and one output, the carry-out memory bit to the next more significant bit.
2018-09-20

## Slide 27: Designing an adder word slice
MCC092 Integrated Circuit Design
Bitslice 6
Bitslice 5
Bitslice 4
Bitslice 3
Bitslice 2
Bitslice 1
Adder word slice
2018-09-20
Notes: This slide shows the datapath layout. We can see that the datapath is designed by 8 more or less identical bit slices, one for each bit. Each bit slice contains different functionalities, at the datapath level we can talk about functionality slices.
This is a design style that we are going to use in this course in some design examples concerning adder design. The use of bit slices to form functional arrays is sometimes referred to as iterative logic arrays, if all bit slices in the array are identical. This is a very efficient way of designing, since we only need to design one bit-slice cell to build a complete multi-bit array.
As I said, we shall apply this design style to the design of a full adder in a series of exercises later in the course.

## Slide 28: Iterative logic arrays: FULL ADDER
MCC092 Integrated Circuit Design
Sum0
Sum1
Sum2
Sum3
FA
a0
Sum0
b0
cin
cout
FA
a0
b0
cin
FA
a1
b1
cout
FA
a2
b2
FA
a3
b3
Sum0
Sum1
Sum2
Sum3
Sum4
Sum5
Sum6
Sum7
FA
a4
b4
FA
a5
b5
FA
a6
b6
FA
a7
b7
Sum4
Sum5
Sum6
Sum7
Adder word slice
2018-09-20
Notes: One of the main themes of this course is the design of n-bit adders. For starters, we will do that by designing the adder as an iterative logic array. For this, we need to design one Full Adder cell as the one shown here. We will use the methods discussed in this lecture to design the cell with MOSFETs from the Boolean truth table.
Then we will build an iterative logic array from many instances of this cell.
The two numbers to be added are enetered at the top. The carry-in is entered to the LSB (least significant bit) to the right. As the carry ripples from cell to cell, from right to left, the sums pop out at the bottom.

## Slide 29: Iterative logic arrays: FULL ADDER
MCC092 Integrated Circuit Design
2018-09-20
FA
a0
b0
cin
cout
a0
Sum0
b0
cin
Carry logic
SUM logic
cout
Prelab design tasks (see prelab 2 instructions):
Design carry logic as a SUM of products!
Draw MOSFET schematic!
Calculate logical effort and parasitic delay of the inverting carry-logic cell that you have designed!
Calculated delay through carry chain
Sum0
Notes: One of the main themes of this course is the design of n-bit adders. For starters, we will do that by designing the adder as an iterative logic array. For this, we need to design one Full Adder cell as the one shown here. We will use the methods discussed in this lecture to design the cell with MOSFETs from the Boolean truth table.
Then we will build an iterative logic array from many instances of this cell.
The two numbers to be added are enetered at the top. The carry-in is entered to the LSB (least significant bit) to the right. As the carry ripples from cell to cell, from right to left, the sums pop out at the bottom.

## Slide 30: Prelab 2
What is still unclear?

## Slide 31: Review from lecture 4: Tapered buffer

## Slide 32: The tapered buffer
Reff/x1
Reference inverter . . .
and two inserted buffer inverters
Reff
Reff/x2
CL=HC
C
x1C
x2C
With two intermediate buffer inverters we obtain a normalized delay relative to tau: D=(pinv+h1)+(pinv+h2)+(pinv+h3)
where we have defined the stage electrical efforts, or fanouts, h.
Here h1=x1, h2=x2/x1, and h3=x3/x2).
We know we must have h1h2h3 = H, So only h1 and h2 are independent variables, the third, h3, becomes h3=H/h1h2.
TASK: Show that minimum delay is obtained for h1=h2=h2=h=3√H >>> D=3(pinv+3√H)
Size x1
Size=1
Size x2
H is the
path electrical effort
Please note that H is the
path electrical effort
while h is the
stage electrical effort.

## Slide 33: The tapered buffer
Reff/x1
Reference inverter . . .
and two inserted buffer inverters
Reff
Reff/x2
CL=HC
C
x1C
x2C
With two intermediate buffer inverters we obtain a normalized path delay:
D=(pinv+h1)+(pinv+h2)+(pinv+H/h1h2).
Taking partial derivatives wrt h1 and h2 we obtain
Size x1
Size=1
Size x2
H is the
path electrical effort
Please note that H is the
path electrical effort
while h is the
stage electrical effort.

## Slide 34: The tapered buffer
Reff/x1
Reference inverter . . .
and two inserted buffer inverters
Reff
Reff/x2
CL=64C
C
4C
16C
Sharing the load equally between the inverters yields equal stage fanouts h=3√64=4
The total delay is then equal to 3 FO4 delays, i.e. 15tau=75 ps (assuming pinv=1).
Size x1=4
Size=1
Size x2=16
Example with path
electrical effort H=64

## Slide 35: The tapered buffer
Solving this problem we start by having derived that minimum delay occurs when stage electrical efforts, h, are equal.
Hence path propagation delay is given by
Furthermore, h=N√H, i.e. H= hN.
Taking natural logarithms we obtain number of inverters
We rewrite path delay equation as
Looking for minimum path delay by taking derivatives of D wrt h
we obtain
Analytical solution is possible only for pinv=0:
h=e=2.72 which gives N = ln H
Note: Derivation inserted for
completeness.
You don’t have to learn to do
this derivation!

## Slide 36: The tapered buffer
For pinv≠0 the equation has to be solved numerically
For typical values of pinv the optimum tapering factor is between 3.6 and 5. Typically a FO4!
Note that the propagation delay minimum is rather flat, while total inverter area on the silicon decreases rapidly when larger stage fanout is used.
Silicon real estate (=cost) can be saved for relatively little loss of speed!
Stage fanout, h
Parasitic delay, pinv
Delay
Area
e
0
5
3
8
1
0
[Hedenstierna & Jeppson 1987]
pinv =1
h=3.6
stage fanout
Normalized delay
Normalized area

## Slide 37: Review from lecture 4: Tapered CMOS inverter stages
H = CL/CIN: path electrical effort
Equal stage electrical effort, h, gives shortest delay
  hoptN = H, where N is number of stages
  That is hopt = N√H
Normalized path delay for path is called Dopt:
Dopt = N×hopt + P, with P sum of all parasitic delay
Dopt = N×hopt + N×pinv
If N not given, select N such that h is close to 4; to save area make h a bit higher than 4.

## Slide 38: CMOS inverter stages with branching
Introducing b = the branching effort
b = (conpath + coffpath)/conpath
b is 1 or larger
Notes: We do not only have to achieve the total scaling up H there are some additional capacitances that have to be driven on the way.

## Slide 39: Path delay with branching
Equal stage electrical effort gives shortest delay
Path effort: F = H×B
  B: path branching effort
  B = b1×b2×b3×…bN-1 (assuming N stages)
  b = (conpath + coffpath)/conpath branching effort
Determine fopt= N√F
Normalized path delay Dopt
  Dopt = N×fopt + P where P is sum of parasitic delay
  Dopt = N×fopt + N×pinv

## Slide 40: Path delay – when (some) gates are not inverters
Equal stage effort still gives shortest delay
  Now includes also logical effort: g
Path effort: F = G×H×B
  G: path logical effort
  G = g1×g2×g3×…gN (assuming N stages)
  B defined as before
Determine fopt as N√F.
Normalized path delay Dopt
Dopt = N×fopt + P, P is sum of parasitic delay
Notes: On the way we have to scale up some more…

## Slide 41: Approach for delay optimization= path sizing
Given: N stages, g and p for all gates + any branching efforts b
Calculate path effort F from F = G×H×B
Calculate stage effort fopt as N√F
(Calculate path delay D = N×fopt + P)
Find gate sizes X2 to XN starting from start or end of path.
  Note that X1 (input capacitance of first stage) does not change!
  Don’t forget to include branching efforts!
Check also that f1 /fN (for the remaining stage) is also fopt so you did not make a mistake!
Read W&H section 4.5.4
For more practical considerations

## Slide 42: Clock tree task from latest exam
Find fopt, Dopt and
the input capacitances at
stages 2 and 3
Work in small groups
Replies in socrative.com room: MCC0922018 as usual
Solution:
fopt = 32/3
Dopt = 38
(assuming pinv = 1)
Stage 3: CIN =
(4/3)× 32C/(32/3) = 4C
Stage 2: CIN =
(4/3) × (4Cx4)/(32/3) = 2C

## Slide 43: Improve delay by adding one inverter stage – how much is path delay improved?
Find new
fopt, Dopt
with added stage
Later you can calculate the sizes too
I will post those numbers
Solution:
F =(32/3)^3
fopt = 4√F≈ 5.9
Dopt = 4 × 5.9 + 7pinv=
30.6 (assuming pinv = 1)
CIN2 = 5.9C
CIN3 = 6.5C
CIN4 = 7.2C

## Slide 44: Summary path delay optimization
Goal: minimize normalized path delay (that is, critical path delay)
Path effort F= G × H × B (general expression for all cases)
path electrical effort: H = CL/CIN (for entire path)
path branch effort: B = b1 × ….. × bN (for entire path)
path logical effort : G = g1 × …..× gN (for entire path)
Optimal stage effort is fopt = N√F
Optimal path delay Dopt is then: Dopt = N × fopt + P
where P is path parasitic delay = sum of all p
Read W&H section 4.5 Logical Effort of Paths

## Slide 45: Conclusion
Review of logical effort muddy issues
Linear model for non-inverting gate
  d + gh, g due to scaling between gate and inverter, p the internal delay
Prelab 2
  Design a carry cell
Review tapered buffer
  hopt, Nopt
  hopt = N√H
  Nopt corresponds to FO4 stage delay but shallow minimum
Path delay optimization
  Path effort: F = GHB
  fopt = N√F
  Dopt = N×fopt + P
  Finding the sizes from start or end of path.